## Slide 1: OSI Protocol Stack
Notes: Given the post man exemple

## Slide 2: Internet structure: network of networks
End systems (clients) connect to Internet via access ISPs (Internet Service Providers)
Access ISPs in turn must be interconnected.
  So that any two hosts can send packets to each other
Resulting network of networks is very complex
  Evolution was driven by economics and national policies

## Slide 3: Protocol “layers”
Networks are complex,
with many “pieces”:
  hosts
  routers
  links of various media
  applications
  protocols
  hardware, software
Question:
is there any hope of organizing structure of network?
…. or at least our discussion of networks?

## Slide 4: Why Layering?
Dealing with complex systems:
    explicit structure allows identification, relationship of complex system’s pieces
  layered reference model for discussion
  Modularization eases maintenance, updating of system
  change of implementation of layer’s service transparent to rest of system
  e.g., change in gate procedure doesn‘t affect rest of system

## Slide 5: ISO/OSI Reference Model
presentation: allow applications to interpret meaning of data, e.g., encryption, compression, machine-specific conventions
session: synchronization, checkpointing, recovery of data exchange
Internet stack “missing” these layers!
  these services, if needed, must be implemented in application
  needed?
application
presentation
session
transport
network
link
physical

## Slide 6: Internet Protocol Stack
Application: Actual job of applications.
Session: Combines independent request-responses to the session logic sometimes reflecting transaction of user, real or virtual.
Transport: Creates multiple parallel application-serving delivery channels (called ports) above each network point.
Network: Delivery across networks: from the sending LAN to the receiving LAN using routing.
Data-Link: Delivery within local network (LAN) between directly connected NICs.
Physical: Transfer of ‘1’ and ‘0’ bits via electro-magnetic media channels: decoding/encoding, signal detection, calibration, channel creation, frequency, power, modulations, etc.
application
transport
network
link
physical

## Slide 7: Internet Protocol Stack
application: supporting network applications
  FTP, SMTP, HTTP
transport: process-process data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet, 802.11 (WiFi), PPP
physical: bits “on the wire”
application
transport
network
link
physical

## Slide 8: Encapsulation
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame

## Slide 9: The Complete Packet
Application Header
Presentation Header
Session Header
Transport Header
Network Header
Data Link Header
Frame Preamble
Data Link Traler(CRC)
Data
Packet

## Slide 10: Packet Components
Header
Data
Trailer
9
Introduction 1-9

## Slide 11: Encapsulation and decapsulation

## Slide 13: Application Layer
The set of (of protocols that supports) applications that use the network
  telnet, ftp, http, smtp, dns, ping, tracert, …
  More ??
Doesn’t provide services to any other layer
Application
Transport
Network
Link
Phy

## Slide 15: Transport layer - Goal: data transfer between end systems
TCP -Transmission Control Protocol [RFC 793]: Internet’s connection-oriented service
  reliable, in-order byte-stream data transfer
  flow control
  congestion control
UDP - User Datagram Protocol [RFC 768]: Internet’s connectionless service
  unreliable data transfer
  no flow control
  no congestion control

## Slide 17: Network Layer
Carries data from source to destination
network layer is provided by Internet Protocol (IP)
found in all end-systems and routers
provides abstraction of end-to-end link
segmentation and reassembly
packet-forwarding, routing, scheduling
unique IP addresses
only best-effort service
chooses which packets to drop
Application
Transport
Network
Link
Phy

## Slide 18: Network Layer
Unicast - piece of information is sent from one point to another point in the network
Multicast - piece of information is sent from one or more points to a set of other points
Broadcast - piece of information is sent from one point to all other points in the network
Application
Transport
Network
Link
Phy

## Slide 20: Link Layer
Reliable communication over a single link
Introduces the notion of a frame
  set of bits that belong together
Internet
  a variety protocols most common is Ethernet
  others are FDDI, SONET, HDLC
Dependent on underlying physical link properties.
Link layer protocols are the lower layer of software
How much wires do we need to allow physical transfer in the classroom for
N-students? N* (N-1)/2.
Application
Transport
Network
Link
Phy
Notes: For 40 students it is 780 wires between all students. Each student will sit with 39 wires – and need to label by name each wire to pass information. This Name Label is actually the identity of the Student's computer – in Networking we use Mac-address.

## Slide 22: Physical Layer
Moves bits between physically connected end-systems
Coding scheme to represent a bit
Internet: technology to move bits on a wire, wireless link, satellite channel etc.
Application
Transport
Network
Link
Phy